## Slide 1: Juniper Apstra 4.2.1 EVE-NG Virtual Lab Demo Video series companion guide Video 7: Day-1 Over-the-top DC Interconnect
Colin Doyle, Sr. CE AMER
See the complete video walkthrough on YouTube at: https://www.youtube.com/@5minutejunos
Ask questions at the Juniper Elevate Community using the hashtag #5minutejunos
Adapted from v4.0.0 documentation originally compiled by: - Raymond Lam, SSE APAC - Tony Chan, SSE APAC

## Slide 2
Agenda
Day-0 Fabric Onboarding
Virtual Device Profile Verification
Virtual Device Profile Cloning
Onboarding Virtual Nodes
Create ASN Pool and IP Pools
Create Logical Devices and Interface Maps
Create Rack Types
Create Templates
Create Blueprints
Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Server Links
Data Center Interconnect
DCI Addendum: Direct Peering
Core/WAN Connectivity
Internet Connectivity
Day-2 Operational Scenarios
Incorrect Cable Patch (RCA, LLDP Link Discovery, Time Voyager)
Config Deviation Checking
Apply custom config through Configlet
View Telemetry Data
Hardware Replacement
Future Documentation
Firewall Service Chaining
  Cluster with Service Block
  Type-5 Route (fabric integrated) with MNHA
VLAN Stitching
vEvo Fabric
Prepping your Lab

## Slide 3: Day-1 Service Provisioning
Create Routing Zones
Create Virtual Networks
Assign Virtual Network to Switchports
Add Testing Hosts
Data Center Interconnect (OTT)
DCI Addendum – Direct Peering
Core Connectivity
Internet Connectivity

## Slide 4
We will be provisioning an Over-The-Top (OTT) DCI for this lab. The border leafs will peer with the external vMX routers to exchange fabric loopback reachability routes. Once the border leafs in each fabric have loopback reachability, we can peer them directly to exchange routes between DC fabrics.
Below diagram illustrates the topology of the data center after this section.
Data Center Interconnect #1 – Underlay
A-spine1
A-spine2
A-border1
A-border2
A-leaf1
A-leaf2
ext-rtr1
B-spine1
B-spine2
B-border1
B-border2
B-leaf1
B-leaf2
ext-rtr2
Unmanaged by Apstra, created in blueprints as external generic systems
eBGP peer, preconfigured in the setup
External links added in this section to exchange loopback address
ge-0/0/3
ge-0/0/3
ge-0/0/3
ge-0/0/3

## Slide 5: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 6: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 7: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 8: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 9: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 10: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 11: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Physical > Topology and click “border_rack_dc_a_001_leaf1”
Click the checkbox for the border rack node and select “Add internal/external generic system”
Create a new external generic system called ext-rtr1, select “None” for the device representation, and click “Next”
Select port 3 on each border leaf, click the port icon followed by the “Add Link” button for each, then click “Create”
Click the "ext-router", open the properties page and edit its ASN, update it to 65001. If you skip this step, Apstra will ask you to assign a ASN resource pool to external generic system at later stage
Go to Blueprints > DC-A > Staged > Policies > Routing Policies, and click “Create Routing Policy”
  Name: ext-router-policy
  Import Policy: Extra Only
  Extra Import Routes:
  Export Policy: Loopbacks only
Prefix | GE Mask | LE Mask | Action
192.168.1.0/24 | 32 |  | Deny
0.0.0.0/0 | 32 |  | Permit

## Slide 12: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 13: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 14: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 15: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 16: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 17: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 18: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 19: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 20: Data Center Interconnect #1 – Underlay
Go to Blueprints > DC-A > Staged > Connectivity Templates and create a new template called "ext-router-ct"
Follow the screenshots to create the connectivity template
Assign the connectivity template to the ge-0/0/3 interface of both border leaf switches
Go to Blueprints > DC-A > Staged > Physical, edit the Link IP’s – To Generic resource, and add the External Link IP Pool
Go to Blueprints > DC-A > Staged > Virtual > Protocol Sessions, get the ASN/IP address of border leaf switches and IP address of external router links

## Slide 21: Data Center Interconnect #1 – Underlay
Commit the Blueprint for DC-A
Repeat the steps for DC-B:
  create an external generic system ext-rtr2
  add two links connecting to ge-0/0/3 of border1 and border2
  assign ASN 65002 to the external router
  create routing policy ext-router-policy (Import “Extra Only”, deny 192.168.2.0/24 GE 32, permit 0.0.0.0/0 GE 32, export only loopbacks)
  create connectivity template ext-router-ct
  assign the connectivity template to ge-0/0/3 of border1 and border2
  assign External Link IP address pool to generic systems
  get the ASN and IP address of border leaf switches and external router
①
②

## Slide 22: Data Center Interconnect #1 – Underlay
Login to ext-rtr1 and ext-rtr2, and then apply interface and routing configuration to establish underlay BGP connectivity to EVPN fabric
ext-rtr1 configuration
set system root-authentication plain-text-password (Juniper)
set system host-name ext-rtr1
delete chassis
set interfaces lo0.0 family inet address 172.31.0.0/32
set interfaces ge-0/0/0.0 family inet address 10.100.100.0/31
set interfaces ge-0/0/1.0 family inet address 10.3.0.1/31
set interfaces ge-0/0/2.0 family inet address 10.3.0.3/31
set routing-options autonomous-system 65001
set protocols bgp group DCI neighbor 10.100.100.1 peer-as 65002
set protocols bgp group ebgp neighbor 10.3.0.0 peer-as 65102
set protocols bgp group ebgp neighbor 10.3.0.2 peer-as 65103
(set local root password)
(set local hostname)
(stop auto-configure script)
(set local loopback address)
(interface to ext-rtr2)
(interface to A-border1)
(interface to A-border2)
(local ASN)
(BGP neighbor to ext-rtr2)
(BGP neighbor to A-border1)
(BGP neighbor to A-border2)

## Slide 23: Data Center Interconnect #1 – Underlay
Login to ext-rtr1 and ext-rtr2, and then apply interface and routing configuration to establish underlay BGP connectivity to EVPN fabric
ext-rtr2 configuration
Login to Spine, Border Leaf, and Leaf switches to verify the route table, you should be able to see the loopback address routes from another data center
set system root-authentication plain-text-password (Juniper)
set system host-name ext-rtr2
delete chassis
set interfaces lo0.0 family inet address 172.31.0.1/32
set interfaces ge-0/0/0.0 family inet address 10.100.100.1/31
set interfaces ge-0/0/1.0 family inet address 10.3.0.5/31
set interfaces ge-0/0/2.0 family inet address 10.3.0.7/31
set routing-options autonomous-system 65002
set protocols bgp group DCI neighbor 10.100.100.0 peer-as 65001
set protocols bgp group ebgp neighbor 10.3.0.4 peer-as 65202
set protocols bgp group ebgp neighbor 10.3.0.6 peer-as 65203
(set local root password)
(set local hostname)
(stop auto-configure script)
(set local loopback address)
(interface to ext-rtr1)
(interface to B-border1)
(interface to B-border2)
(local ASN)
(BGP neighbor to ext-rtr1)
(BGP neighbor to B-border1)
(BGP neighbor to B-border2)

## Slide 24: Data Center Interconnect #1 – Underlay

## Slide 25
After exchanging the loopback addresses between data centers, we will create a remote EVPN gateway in each blueprint to establish the EVPN BGP sessions between border leaf switches.
The below diagram illustrates the topology of the data center after this section.
Data Center Interconnect #2 – Overlay
A-spine1
A-spine2
A-border1
A-border2
A-leaf1
A-leaf2
ext-rtr1
B-spine1
B-spine2
B-border1
B-border2
B-leaf1
B-leaf2
ext-rtr2
OTT EVPN BGP sessions created in this section to exchange EVPN routes

## Slide 26: Data Center Interconnect #2 – Overlay
Repeat for DC-B by recording DC-A’s loopback and ASN assignments
Go to Blueprints > DC-B > Active > Physical > Nodes and note the Loopback IP’s and ASN’s for the border leaf switches
Go to Blueprints > DC-A > Staged > DCI > Over the Top or External Gateways, click “Create Over the Top or External Gateway” button, then define the border leaf switches in DC-B as the remote EVPN gateways using the following table
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
B-border1 | 192.168.2.2 | 65202 | border_rack_dc-a-001_leaf1
B-border2 | 192.168.2.3 | 65203 | border_rack_dc-a-001_leaf2

## Slide 27: Data Center Interconnect #2 – Overlay
Go to Blueprints > DC-B > Active > Physical > Nodes and note the Loopback IP’s and ASN’s for the border leaf switches
Go to Blueprints > DC-A > Staged > DCI > Over the Top or External Gateways, click “Create Over the Top or External Gateway” button, then define the border leaf switches in DC-B as the remote EVPN gateways using the following table
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
B-border1 | 192.168.2.2 | 65202 | border_rack_dc-a-001_leaf1
B-border2 | 192.168.2.3 | 65203 | border_rack_dc-a-001_leaf2

## Slide 28: Data Center Interconnect #2 – Overlay
Go to Blueprints > DC-B > Active > Physical > Nodes and note the Loopback IP’s and ASN’s for the border leaf switches
Go to Blueprints > DC-A > Staged > DCI > Over the Top or External Gateways, click “Create Over the Top or External Gateway” button, then define the border leaf switches in DC-B as the remote EVPN gateways using the following table
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
B-border1 | 192.168.2.2 | 65202 | border_rack_dc-a-001_leaf1
B-border2 | 192.168.2.3 | 65203 | border_rack_dc-a-001_leaf2

## Slide 29: Data Center Interconnect #2 – Overlay
Go to Blueprints > DC-B > Active > Physical > Nodes and note the Loopback IP’s and ASN’s for the border leaf switches
Go to Blueprints > DC-A > Staged > DCI > Over the Top or External Gateways, click “Create Over the Top or External Gateway” button, then define the border leaf switches in DC-B as the remote EVPN gateways using the following table
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
B-border1 | 192.168.2.2 | 65202 | border_rack_dc-a-001_leaf1
B-border2 | 192.168.2.3 | 65203 | border_rack_dc-a-001_leaf2

## Slide 30: Data Center Interconnect #2 – Overlay
Go to Blueprints > DC-B > Active > Physical > Nodes and note the Loopback IP’s and ASN’s for the border leaf switches
Go to Blueprints > DC-A > Staged > DCI > Over the Top or External Gateways, click “Create Over the Top or External Gateway” button, then define the border leaf switches in DC-B as the remote EVPN gateways using the following table
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
B-border1 | 192.168.2.2 | 65202 | border_rack_dc-a-001_leaf1
B-border2 | 192.168.2.3 | 65203 | border_rack_dc-a-001_leaf2

## Slide 31: Data Center Interconnect #2 – Overlay
Go to Blueprints > DC-B > Staged > DCI > Settings, click “Modify Settings” button, and change the ESI MAC msb value from 2 to 4
Go to Blueprints > DC-B > Staged > DCI > Over the Top or External Gateways and create EVPN BGP sessions between the local border leafs and the border leafs in DC-A
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
A-border1 | 192.168.1.2 | 65102 | border_rack_dc-b-001_leaf1
A-border2 | 192.168.1.3 | 65103 | border_rack_dc-b-001_leaf2

## Slide 32: Data Center Interconnect #2 – Overlay
Go to Blueprints > DC-B > Staged > DCI > Settings, click “Modify Settings” button, and change the ESI MAC msb value from 2 to 4
Go to Blueprints > DC-B > Staged > DCI > Over the Top or External Gateways and create EVPN BGP sessions between the local border leafs and the border leafs in DC-A
Commit the Blueprint
Name | IP Address | ASN | Local Gateway
A-border1 | 192.168.1.2 | 65102 | border_rack_dc-b-001_leaf1
A-border2 | 192.168.1.3 | 65103 | border_rack_dc-b-001_leaf2

## Slide 33
Congratulations! You have built a simple, single-tenant, multi-fabric Apstra lab! The intent of your operational fabrics are shown below.
The following sections focus on enhancements to your lab such as direct DCI peering between spines, WAN/Core connectivity, and some business value demonstrations focused on common operational scenarios.
Initial Setup Complete!
DC-A Blueprint
vn101 (192.168.101.0/24)
vn102 (192.168.102.0/24)
A-bms-3
To A-leaf1
ge-0/0/9
To A-leaf2
ge-0/0/8
To A-leaf1
ge-0/0/7
To A-leaf2
ge-0/0/7
To A-leaf1
ge-0/0/8
ae1
ae2
A-bms-1_bridge
A-bms-2_bridge
vSRX
Tenant-1 Routing Zone
DC-B Blueprint
Tenant-1 Routing Zone
To B-leaf1
ge-0/0/7
To B-leaf2
ge-0/0/7
ae1
B-bms-1_bridge
vSRX
To B-leaf1
ge-0/0/8
To B-leaf2
ge-0/0/8
ae2
B-bms-2_bridge
vSRX
vn101 (192.168.101.0/24)
vn103 (192.168.103.0/24)
vSRX
Stretch L2 OTT DCI
A-bms-2
192.168.102.22
A-bms-1
192.168.101.11
uMate
uMate
B-bms-1
192.168.101.44
uMate
B-bms-2
192.168.103.55
uMate
192.168.101.33