## Slide 1
AREA 0
AREA 1
R2
R1
SWs
R3
PCs
PCs
PCs
Services
Services
Services
tunnels
Services
Services
Services
Services
Services
Services
Services
Services
Services
OK, so if I am understanding this better, this is what you used to have:
p2p

## Slide 2
AREA 0
AREA 1
R2
R1
SWs
R3
PCs
PCs
PCs
Services
Services
Services
Services
Services
Services
Services
Services
Services
Services
Services
Services
Networks 1
Networks 2
Networks 3
OSPF
p2p
tunnels
(p2p)
Which we can represent like this:
I am calling the networks connected to R1, R2 and R3, networks 1, networks2, and networks 3, and just adding an example subnet.
Example 10.1.1/24
Example 10.2.2/24
Example 10.3.3/24

## Slide 3
I think you are trying to solve routing, AND isolate traffic from that new network going to the services behind R1 with OSPF. You should solve them separately, and likely you don’t need the routing instance (though it is possible, yet more complicated as you might need to share routes between tables and so on)
So, I would go back to the original design, and use security policies on R3, to control who can access the services behind R1 and who can’t. And here is the next set of questions for you (routing):
When you say “I put the switch and at the L2 level I divided one tunnel into two” How did you do this at L2?
I thought you had TWO separate tunnels R1R3, and R1R2, is that the case?
Then you should have OSPF neighbors between each pair of routers. Each router should have 2.
I suspect that was the case because you said “Router 1 saw the network (which I assume is network3 in my picture) along the upper tunnel”.
Now you also say: “router 3 saw some services behind router 1 through router 2 and responded to requests to it, and not to router1
  Two possible reasons I can think of:
Both R1 and R2 are advertising the same subnets. Imagine that instead of 10.1.1/24 and 10.2.2/24, they both advertise 10.1.1/24. Then, R3 is learning about the same subnets from R1 and R2, and choses only on3 at random (Junos does not do load balancing by default and choses only one next hop when the metric is the same).
Something like this:
10.1.1.0/24 *[OSPF/10] 00:01:28, metric 1
to 10.20.1.2 via st1.0
> to 10.20.4.2 via st2.0 (selected next-hop)
2) The metrics are not configured correctly so the metric to get to 10.1.1.0/24 from R3 is better via R2:

## Slide 4
Zone
R1_SERVICES
Zone
R2_SERVICES
ZONE USERS
R2
R1
SWs
R3
PCs
PCs
PCs
Services
Services
Services
Services
Services
Services
Services
Services
Services
Services
Services
Services
Networks 1
Networks 2
Networks 3
p2p
For the isolation part I would use security policies. Something like this. Make sure OSPF is allowed in the security zones, and the st interfaces are configured in the zones and all that.
Example 10.1.1/24
Example 10.2.2/24
Example 10.3.3/24
[edit security policies from-zone USERS to-zone R1-SERVICES]
lab@vSRX1# show | display set relative
set policy 1 match source-address USER-NEW-NETWORK
set policy 1 match destination-address R1-SERVICES
set policy 1 match application SERVICES
set policy 1 then permit
Anything not explicitly permitted it rejected by the default policy